## Slide 1: Techno-Economic Analysis for ARPA-E Performers
Alex Luce

## Slide 2: Agenda
  Motivation
    Techno-Economic Analysis (TEA) is essential tool for ARPA-e team & Performers
  Background: Current TEA activity at ARPA-e
    Process is currently ad-hoc and fragmented
    Several models already exist in certain areas
  Scope of Work
    Research energy technology archetypes
    Streamline process for creating TEAs
  Outcomes
    Providing best-practices and templates for technology archetypes.
    Provide program-specific TEAs as examples
Notes: Project descriptions should have already been provided; you can also find them under P: Technology-to-Market/Internships 2013/Project Descriptions.

## Slide 3: Executive Summary
  Motivation
    Techno-Economic Analysis (TEA) is essential tool for ARPA-e team & Performers

## Slide 4: Proposed Video Modules
Background: What is a TEA and how is it used?
Getting Started: How to build a TEA for the first time
  Checklist: Steps before you start modeling
  Assumptions
  Process flow diagram
Best Practices for a useful model
  Gathering information
  Dealing with uncertainty
  Incorporating feedback
Using your model to inform technical and business decisions
  Basic sensitivity analysis
  real-life examples

## Slide 5: Table of Contents
Background:
  What is Techno Economic Analysis
  How is Techno Economic Analysis used at ARPA-E?
Getting Started: How to build a TEA for the first time
  Checklist: Steps before you start modeling
  Assumptions
  Process flow diagram
Best Practices for a useful model
  Gathering information
  Dealing with uncertainty
  Incorporating feedback
Using Techno Economic model to inform technical and business decisions
  Basic sensitivity analysis
  real-life examples
Appendix and Resources
(hyperlinked to sections)

## Slide 6: What is techno economic analysis?
Background

## Slide 7: Techno Economic Analysis (TEA)
Identify specific technology improvements that affect major cost drivers
Determine economic viability of end product
More than a Cost Model, not a business plan
Inherently challenging and interdisciplinary
Low Fidelity at Start of Project  Increasing Fidelity as Project Advances
Connects Research Outcomes to Relevant Economic Factors
Notes: Identify specific technology improvements that affect major cost drivers.
Determine economic viability of end product

## Slide 8: Techno Economic Analysis
Nomenclature and modeling specifics will depend on type and stage of problem being considered.
Manufacturing cost
Process design and analysis
Systems cost analysis
Lifecycle cost analysis
Technical cost modeling
can also be known as:
Source: NREL, Technology Systems and Sustainability Analysis Group

## Slide 9: Techno Economic Analysis
1. Getting first significant digit close is challenge
2. It is OK to say: we don’t know ‘X,Y,Z’ at this time
  Defined by ultimate market goal
  Achieve consistency in credibility and objectivity
  TEA should be discussed – look at entire ecosystem
  TEA should capture risk
  Assumptions need to be transparent and credible
Overarching principals:
Source: Internal Analysis & NREL, Technology Systems and Sustainability Analysis Group

## Slide 10: Example TEA: Solar PV Panel
Key Metric:
$/watt  …LCOE
System costs:
$/m2 (cell components) + $m2 (hardware components) + $/kW (inverter)
/system lifetime
Unknowns:
Degradation, temperature coefficient
Manufacturing processes
Cost of raw materials and labor
Installation, permitting
Taxes
…at the end of the day it’s all about LCOE (the cost of electricity produced)
Now
$1/watt
(goal)
TEA goes beyond cost modeling by connecting research outcomes to economic factors

## Slide 11: Basics of a technical cost/performance model
Design tradeoffs affect both cost and performance
Technical Cost Modeling combines cost modeling with physical process models
External
Inputs
Part Size
Material
Volume/yr
Predicted
Parameters
Gas Composition
Deposition Rate
Equipment Utilization
Cost & Performance Outputs
Material Costs
Energy Costs
Equipment Costs
Performance Metrics
Source: Szekeley, JOM (1996) http://www.tms.org/pubs/journals/jom/9612/szekely-9612.html
Example:

## Slide 12: TEA modeling interrelationships
Multi-scale, systems model,
Connects: physical performance to production, operation cost
Requires several interconnected models
Performance
Cost
Financial
electrical
structural
chemical
mechanical
bill of materials
Market
Capital
capital
operations
Techno economic analysis
Source: Dan Matuzak

## Slide 13: How ARPA-E Performers use TEA models
Crucial tool for technical and business decision making
Integrate calculations together for holistic consideration
Identify cost, performance drivers  steer research
Communicate results with stakeholders
  Internal: R&D, Management, Marketing
  External: Industry Advisors, Investors, Customers, Licensing Partners
Study system-level impacts of technical details
Notes: -We talked a bit about cost modeling, trying to turn a profit in future; important to you now because it enables R&D
-Each individual calculation may be simple, the real value comes in bringing them all together into one place, efficiently study system-level impacts of technical details
-Most importantly, will identify cost drivers, use this to guide research; best use of your time when addressing cost and performance simultaneously
-Communicate with stakeholders: convince research team members; something concrete to talk about when checking your understanding with industry advisors; know the value so you can negotiate effectively with investors, customers, licensing partners; compelling case for next funding opportunity
-Mature tech companies use cost modeling extensively; once you have it you’ll never stop using it

## Slide 14: TEA use at ARPA-E depends on program stage
Pre-FOA
Award Period
Program scoping:
Does this make sense?
Practical implications
If we do this- will it matter?
What ideas to actually focus on?
Pitch - program justification
Develop high-fidelity tech-specific model
Inform technical and business decisions
Keep performers on track
Program criteria
FOA targets
Evaluate proposals:
Will this hit FOA target?
Compare applications relative to each other
FOA
Establish scientific and technical milestones
Negotiations
Program Stage
early
advanced
Notes: Consider Updating

## Slide 15: TEA evolution during award period
Technical Risk
Award Period (months)
0
12
24
36
Model Fidelity
Basic BOM
Ingredients?
link to performance data or predictions
Process cost model
  Resources required to produce at scale?
  10-20 tab version
  80% of teams
Full financial
company model
How do we make money?
Advanced stage
20% of teams get here
Cost/performance model
Key drivers?
Block diagram –
process flow
simple, 1-2 tabs
All teams
Notes: Process: Determine resources (and $$) required for at-scale production/operation; Tabulate material/component flow, labor & energy use, equipment, etc

## Slide 16: TEA is a discussion tool
  Scientifically driven approach: collecting data, defining variables,
  quantifying uncertainty, testing hypotheses.
Building model is iterative and scientifically driven process
ARPA-E
Program Directors
T2M Team
Provide feedback, insight, industry knowledge
Critical review of model
Sounding board for assumptions
Guidance and comparison
Significant costs?
Performers
PI’s, Scientists, Biz Dev
Build model to inform technical and business decisions
Validate numbers through discussion with industry
Begin to establish supplier relationships
Evaluate impact on potential purchasing decisions
TEA enables focused dialog regarding technology and cost drivers
Notes:   Scientific aspect: collecting data, defining variables, quantifying uncertainty, building a model.

## Slide 17: What currently exists?
Resources, examples, state of the art

## Slide 18: Methods of manufacturing cost estimation
Type | Description | Used | Fidelity | Ease of use | ARPA-e Suitable | Resources
Traditional Cost Accounting | indirect cost = (arbitrary %)*direct cost | General accounting, all over, outdated |  |  |  | 
Cost of Ownership (COO) | per piece of equipment, per lifetime of equipment | Intel, Sematech, microelectronics industry |  |  |  | 
Activity Based Costing (ABC) 1 | Identify direct and indirect cost of production activities; Allocate cost per activity | Management accounting; large firms |  |  |  | 
Technical Cost Modeling 2 | Couple descriptive cost model + predictive technical model | Materials production: process/product oriented |  |  |  | 
Process Based Cost Modeling (PBCM) 3,4 | Maps technology description to process cost | Operations research, mfc./ process optimization |  |  |  | 
0th Order, Research Approach 5 | 1) Consider implications for materials targets, performance tradeoffs; build iterative model. | Internally, ad-hoc |  |  |  | 
Traditional methods can’t forecast cost of new designs, materials, or architectures
Source: 1) Kaplan and Burns (1987), 2) Szekeley (1997), 3) Field (2007), 4) Fuchs (2010), 5) Gur (2014)
*
* Dependent on maturity, assumptions, and stage.
*
Notes: Traditional: http://en.wikipedia.org/wiki/Indirect_costs#Indirect_vs_direct_costs
Szekeley: http://www.tms.org/pubs/journals/jom/9612/szekely-9612.html
Field: http://ardent.mit.edu/real_options/RO_current_lectures/ESD%2003%20Slides/ProcessCostModel03.pdf

## Slide 19: TEA model landscape
Fidelity
Low
High
Transformational
(ARPA-e relevance)
Size of bubble = applicability to multiple teams
Low
High
Argonne Li-ion
battery model
MIT PV Cost Calc.
Example
production cost model
METALS
calculator
REMOTE
calculator
NREL SAM
Process-based
cost model
Electrofuels
model
Investment financial models
= ARPA-E = others
NREL Biorefinery
(Aspen Plus)
early-stage
performer models

## Slide 20: Process Based Cost Modeling
Inform technical decisions before investments are made
Makes connection between technical changes and production cost
Stage 1
Technology Description
Processing Requirements
Source: Source: Erica Fuchs, Randolph Kirchain, Frank Field
Process Model
Operations Model
Financial Model
Stage 2
Stage3
Inputs
Outputs
Steps
Operating Conditions
Resource Requirements
Factor Prices
Productions Cost

## Slide 21: Process of building TEA
  Done for mature technology
  Little value for early-stage tech
Current resources:
  Process-Based Cost Modeling
“Big complex model adapted for a small system”
Generic mfc. “widget” production
Research approach - 0th Order
  What are implications for materials targets, performance tradeoffs, etc.??
  Scientific aspect:
  Collect data, define variables, quantify uncertainty
“Few resources exist”
Performers with early-stage technology will likely be taking the 0th Order Research Approach, its scientifically driven approach.

## Slide 22: Best Practices

## Slide 23: Modeling techniques: cataloging variables and assumptions
Performance variables
Cost assumptions
Manufacturing assumptions
physics
thermodynamics
Dimensionality
Physical Constraints
materials
Yield
Utilization
equipment
chemicals
Project Assumptions
chemistry
biology
labor

## Slide 24: Collecting/Estimating Prices
Price inputs have varying accuracy and use depends on model stage.
Illustrative example
Chart: 
| raw materials | specialty supplier | volume supplier | market research | published or prior work | vendor quotes | negotiated prices
 | 10 | 100 | 70 | 50 | 40 | 25 | 20
Price
Here we see that the price of a material or chemical can vary wildly depending on where the information is obtained. Pay attention to the inherent uncertainty of prices obtained via different sources.
Example | Commodity Prices | Sigma-Aldrich | Alibaba | Lux Research | Academic/ Technical Literature | Vendor | Vendor
Notes: start with raw materials, add multiplicative factor, then sigma aldrich, then volume pricing, then market research, published work, then vendor quotes, then negotiated prices
specialty

## Slide 25: Dealing with uncertainty
Concern:
  “It’s too early—there is too much uncertainty to determine what this would cost”
Modeling still beneficial:
  Make uncertainties explicit
  Identify most valuable improvements
  Develop targets, metrics
  Bound with theoretical limits
  Create thought framework for reducing uncertainties
Cost
+
Performance
Max
Min
Baseline
Notes: -Possible concern: “It’s too early”
-Still beneficial—start simple, and with a little bit of homework get a pretty decent ballpark estimate, that might be enough to indicate what to work on
-See what information you are missing, figure out what you need to know
-Within the framework, see the relationships among all the pieces, improve your understanding of the technology and its uses

## Slide 26: Dealing with uncertainty : sensitivity analysis
Use iterative approach to refine model
Focus on attacking the right problem
Chart: 
| III-V Cell Cost (10000 $/m2) | Concentration (300 x) | PV Cell Efficiency (0.35 ) | Packaging Markup (1.5 ratio) | Optical Thickness (0.2 cm) | Volume percent PC (0.9 ) | Optical Efficiency (0.9 )
III-V Cost/Performance Sensitivity (baseline: 0.37 $/watt) | 0.25748 | 0.27952 | 0.28599 | 0.29417 | 0.3309 | 0.36387 | 0.35971
60000 | 1.47 | 0.80862 | 0.42899 | 0.49028 | 0.58858 | 0.40612 | 0.41367
High priority
Low priority

## Slide 27: Contribution of processing and materials costs
Chart: 
| Metals Processing | Fuels | Li-Ion Battery | Solar Cell | LCD Display
BOM | 10 | 17 | 50 | 55 | 90
Utilities | 80 | 30 | 9 | 5 | 5
non-BOM | 10 | 8 | 41 | 23 | 5
Installation | 0
Is your product driven by processing costs or materials costs?
BOM
Utilities
Sources: 1) METALS calculator tool; 2) REMOTE calculator tool; 3) Argonne National Lab; 4) MIT PV Cost Calculator; 5) Display Search Intl.
100%
BOM = Bill of Materials; Utilities= water, gas, electricity; Other= everything else incl: processing, labor, equipment, etc..
Other
Process-
Driven
Device-
Driven
eg. power, chemical industries
eg. widget production, fully-optimized manufacturing
Cost breakdown mix determines TEA development

## Slide 28: Program technology archetype categorization All TEA’s will have common steps as a starting point
Process-
Driven
Technologies
Device-
Driven
Technologies
Chemical processing, refining
Energy intensive
Materials and process streams,
mass/energy balance
Constructing hardware, systems, devices
Materials intensive
Discrete components, systems integration
Common Steps
Objective: what problem are we solving?
Constraints and boundary conditions
Process flow block diagram
Materials, Labor, Energy, Equipment for each step
Understand and quantify uncertainty

## Slide 29: TEA checklist Before you even open excel
Define the scope of problem |  | Diagram the problem |  | Sanity Check
 |  |  |  | (with T2M Advisor)
Clearly defined question that the model seeks to address? Yes Boundaries defined to limit scope of problem? Yes Assumptions are clearly stated? Yes Key variables? Are defined Have confidence interval High, low, baseline values based on data, literature. System performance: Model Predicted results Experimental results |  | Draw a process flow diagram Yes Draw material flows into AND out of each step: Yes Catalog for each step: Equipment (Q) Labor (L) Energy (E) Expected process yield? Best guess Empirical data Are there any waste streams? Yes No |  | Confirm Assumptions Do assumptions make sense? Resources What informational resources are needed? Can you use analogs from existing work, other sectors/industries? Hypothesis Clearly stated

## Slide 30: Why use a checklist for TEA development?
Break down complex tasks
steer towards simplicity
expected minimum steps
Knowledge sharing
take time to document common processes
memory recall
Accountability
culture of accountability and transparency
N Engl J Med 2009
Checklist impacts many aspects of project including collaboration, communication, and quality of output
Short, limited to critical steps only…
Takeaways
Notes: Figure 4 The WHO Surgical Safety Checklist was tested in eight hospitals in eight different countries, representing both resource-rich and resource-poor populations

## Slide 31: example checklist from METALS TEA
“Lets us avoid walking in the dark with performers…”
Source: METALS_toolv1.xls
Made available for all teams during program inception
Standard method, assumptions, vocabulary
Allows for apples-to-apples comparison of teams
Notes: “Tech SETA’s don’t have time to scrutinize all the stream tables, etc…”

## Slide 32: TEA evolution during award period
Be as smart as possible along every step of the way
Technical Risk
Award Period (months)
0
12
24
36
Model Fidelity
Basic BOM
link to performance data or predictions
Process cost model
  Resources required for producing at scale?
  10-20 tab version
  80% of teams
Full financial
company model
Advanced stage
20% of teams get here
Simple cost/performance model
Block Diagram –
process flow
simple, 1-2 tabs
All teams
Check:
Basic
Assumptions
Check:
Process-flow diagram,
mass/energy balance
Check:
Mfc., waste, yield, utilization
Check:
financial assumptions

## Slide 33: Conclusion

## Slide 34: Performer Toolkit
Enable better assumptions, test hypothesis
BOM & Sensitivity Analysis
Process & Production
Cost Modeling
Resources, Examples, and Bibliography
Chart: 
| III-V Cell Cost (10000 $/m2) | Concentration (300 x) | PV Cell Efficiency (0.35 ) | Packaging Markup (1.5 ratio) | Optical Thickness (0.2 cm) | Volume percent PC (0.9 ) | Optical Efficiency (0.9 )
III-V Cost/Performance Sensitivity (baseline: 0.37 $/watt) | 0.25748 | 0.27952 | 0.28599 | 0.29417 | 0.3309 | 0.36387 | 0.35971
 | 1.47 | 0.80862 | 0.42899 | 0.49028 | 0.58858 | 0.40612 | 0.41367
Cost/Performance
Sensitivity Tool
Resources needed to build product
Knowledge base for performers and ARPA-e team
Manufacturing
Production Line
Bill of Materials
Process Flow
Process Step
(Inputs)
(Outputs)
Opex
Parameters
(2) Capex
Parameters
Output
Cost &
Performance
Summary
Consequences
Current Best Practices

## Slide 35: Conclusion and recommendations
In sum: TEA is an essential tool, but need to continually address possible roadblocks
“Reduces technical uncertainty limits to private sector investment”
-ARPA-E
“Can enable first market opportunities before ultimate program goal”
-ARPA-E
“Can help teams learn ‘bad news’ sooner”
-ARPA-E
“We’re glad you forced us to do this”
-Performer
“We’re a startup with limited bandwidth, we need to focus on research”
-Performer
“Few resources exist”
-ARPA-E
“Its too early to think about cost”
-Performer
“I had no idea where to get started;
Google wasn’t exactly helping”
-Performer
Process of building TEA is beneficial…
… but there are significant challenges

## Slide 36: APPENDIX

## Slide 37: Proposed Video Modules
Background: What is a TEA and how is it used?
Getting Started: How to build a TEA for the first time
  Checklist: Steps before you start modeling
  Assumptions
  Process flow diagram
Best Practices for a useful model
  Gathering information
  Dealing with uncertainty
  Incorporating feedback
Using your model to inform technical and business decisions
  Basic sensitivity analysis
  real-life examples

## Slide 38
Bill of Materials
Unit
Production Cost
$ Operating inputs:
eg. Fuel/Energy
Unit Operating cost
Production
Material/energy
utilization efficiency
Utilities
Labor
Rent
Waste
Stream
Equipment
Machinery
Facilities
CapEx
OpEx
Cost of Goods Sold (COGS) $
Operation
$ Resources for at-scale operation
Performance Analysis
Cost Analysis
Requisite Operating inputs:
eg. Fuel/Energy
Technology Operating
Performance Characteristics
Efficiency, Lifetime, Capacity Factor
Useful Work/Energy
Output
Relevant Performance Metric
(power, energy, etc.)
Waste
Energy/heat
COGS ($)
Performance
Figure of Merit =

## Slide 39: Process of building TEA
Generic mfc. “widget” production
  Done for mature technology
  little value for early-stage tech
“Big complex model adapted for a small system”
Current resources:
  . Process-Based Cost Modeling
Research approach - 0th Order
  What are implications for materials targets, performance tradeoffs, etc.??
  Scientific aspect: collecting data, defining variables, quantifying uncertainty, building a model.
Few resources exist

## Slide 40: Bibliography

## Slide 41: Collecting/Estimating Prices
Process modeling has yielded metrics that can be priced (warehouse square footage, gold usage per day, etc.)
Depending on the sophistication of your cost model, you will need varying accuracy in your price inputs.
Try to understand the variability inherent in estimating prices
Free
Internet Sources
Market Reports and Vendor Discussions
Vendor Quotes
Negotiated Prices
Notes: start with raw materials, add multiplicative factor, then sigma aldrich, then volume pricing, then market research, published work, then vendor quotes, then negotiated prices
graph uncertainty, illustrative example wawterfall

## Slide 42: Remarks to performers
Get started modeling cost early, and refine as knowledge advances
  guess as placeholder to get framework in place (and make note of it)
  work on larger factors first (getting first significant digit right is a challenge)
Use, manipulate, and adapt the template spreadsheet to suit your needs, but
  be guided by its scope (deliberate)
  don’t dodge necessary considerations because of difficulty to validate or seemingly unfavorable results
Full business financial model (cash flow, debt, timing, etc.) also needed before pitching for external financing (not shown here)
Send any cost modeling questions & comments to your ARPA-E Tech-to-Market Advisor

## Slide 43: Background: Basic Cost Modeling
  Purpose Of A Cost Model Is To Inform Technical Decisions
  Incorporates Technical Information About Process
  Builds Cost Up From Technical Detail
  Must Be Able To Address Cost Implications Of Change In
    Product Design or
    Process Operation -- Including Production Volume
A simple cost model can be a useful starting point for building a Techno Economic Analysis.

## Slide 44: What is Cost Modeling?
Recipes
Procedures
Raw Material Prices (est.)
Energy Prices (est.)
Labor Prices (est.)
+ Assumptions!
Inputs
Costs
COST
MODEL
Operating Cost
  Raw Materials
  Labor
Capital Cost
“Fully-Loaded” Cost
Source: Cost Modeling, Chiverton

## Slide 45: Example Cost Model: Solar PV Panel
Key Metric:
$/watt
System cost:
$/m2 (cell components) + $m2 (hardware components) + $/kW (inverter)
/ system lifetime = ____ $/watt
What would this product cost?
Now
$1/watt
(goal)
A simple cost model is a methodology to convert what is known about a product or production process and estimate what the product will cost to produce at scale

## Slide 46: Levels of Performer Cost Modeling
Basic bill of materials (BOM)
    What goes into my technology?
Block diagram of production process
  How is it made?
Production cost model
  What resources are required for producing at scale?
Full financial company model
  How do we make money and run a business?

## Slide 47: Cost Modeling Process Overview
Identify potential cost drivers
Specify functional forms
Find analogous systems
Collect data
Normalize data

## Slide 48: 1. Identify potential cost drivers
  Determine what causes the cost of each element
    Reach out to experts: government, industry, trade associations.
    Distill major cost drivers:
      Technology
        Equipment/production yields, automation, analogs.
        New, high-risk technology is generally more expensive
      Size
        Eg weights, volume, watts, quantity, etc.
        Generally, bigger is more expensive.
      Performance
        Speed, resolution, throughput, reliability.
        Greater performance usually comes at higher cost.

## Slide 49: 2. Specify functional form
What will it look like?
Functional form should make sense
Get engineering opinions if possible

## Slide 50: Steps to Create Process-Based Cost Model
Define Question To Be Answered
Refine Model Boundaries
Diagram Process Operations & Material Flows
Relate Cost To What Is Known
Understand Uncertain Characteristics

## Slide 51: Selecting Analogous Systems
An analogous system will have a similar cost driver and similar functional form when mapped to the cost.
Look for systems that smell, taste, and look like the items you are estimating.
  Example: using flat panel LCD technology to model advanced electro-optic devices for solar
In reality, there may be few systems that employ similar technology, performance, and size – use judgement.
Don’t overly constrain yourself when selecting analogous tasks.

## Slide 52: Collecting Data
Select systems relevant to the system being costed
  Does cost data exist for any compenets you are using?
  Or choose analogous systems or components
Typical cost drivers include physical and performance characteristics:
  Physical characteristics: weight, volume, number of holes drilled, number of parts to assemble, materials and precursor selections, etc.
  Performance characteristics: power, thrust, bandwidth, range, speed, capacity, etc.
Historical improvements in technology are an important consideration
  Know your industry: trends, macro-drivers, change in composition as technology evolves (eg. Increasing percentage of composite materials used in place of metals)

## Slide 53: Basic bill of materials (BOM)
  What goes into my technology?
Simple Battery Example
Anode
Cathode
Separator
Electrolyte
Housing

## Slide 54: Basic bill of materials (BOM)
  What goes into my technology?
Simple Battery Example
Anode
Cathode
Separator
Electrolyte
Housing
Chart: Simple Battery Cost
| Anode | Cathode | Separator | Electrolyte | Housing
Anode Cathode Separator Electrolyte Housing | 100 | 50 | 5 | 20 | 12.5
A bill of materials is a list of items needed to build a product correctly.

## Slide 55: TEA Examples
Biorefinery (NREL)
  http://www.nrel.gov/extranet/biorefinery/aspen_models/
  Includes TEA excel spreadsheets
Li-Ion Battery Cost-Performance Model (Argon) BatPac
  http://www.cse.anl.gov/batpac/index.html
Solar PV
  Crystalline silicon cost model paper and excel files: http://pv.mit.edu/tma/

## Slide 56: 5 M’s of Manufacturing
Materials |  |  |  | 
Manpower |  |  |  | 
Methods |  |  |  | 
Machines |  |  |  | 
Measurements |  |  |  | 
+rate, quantity, efficiency.

## Slide 57: Fundamental Cost Tradeoffs in Production
Development | Material | Fabrication | Assembly
Time & Complexity Sharing among related systems Novelty vs. incremental refinement | Raw materials cost Ability to reuse scrap and process materials Properties and performance Purity of materials used and level of processing required | Feasible geometries and complexity Final product properties Rates of production, utilization, loss, defects, rework Tooling & equipment requirements | Number of parts Diversity of processes and materials Rates of production, loss, defects, rework Tooling & equipment requirements
Source: Field, JOM (2007)

## Slide 58: Block diagram of production process
How is it made?

## Slide 59: To understand cost development the industry structure needs to be understood
Example: Li-Ion battery supply chain overview*
Adapted from: Roland Berger "LIB value chain cost model"
Anodes
Cathodes
Cell/Battery Makers
Separator
Electrolyte Solution
Binder
End-product makers
Co
Copper foil
Anode
Cathode materials
Cobalt
Aluminum Foil
Separator manufacturers
Electrolyte Solution
Electrolyte

## Slide 60
Bill of Materials
Unit
Production Cost
$ Operating inputs:
eg. Fuel/Energy
Unit Operating cost
Production
Material/energy
utilization efficiency
Utilities
Labor
Rent
Waste
Stream
Equipment
Machinery
Facilities
CapEx
OpEx
Cost of Goods Sold (COGS) $
Operation
$ Resources for at-scale operation
Performance Analysis
Cost Analysis
Requisite Operating inputs:
eg. Fuel/Energy
Technology Operating
Performance Characteristics
Efficiency, Lifetime, Capacity Factor
Useful Work/Energy
Output
Relevant Performance Metric
(power, energy, etc.)
Waste
Energy/heat
COGS ($)
Performance
Figure of Merit =

## Slide 61: Price – COGS = Gross Margin
Chart: 
Price | 100
Material | 30
Depreciation | 15
Labor | 3
Other | 2
Gross Margin | 50
COGS
Definitions
Price – What the market pays
COGS – Cost of Goods Sold
  Materials
  + Depreciation
  + Labor
  + Other
COGS the full cost to manufacture your product
  includes materials, depreciation, labor, other costs and is impacted by yield, utilization
BOM – Bill of Materials, applies to single unit
Note: Materials ≠ BOM

## Slide 62: COGM = Cost of Goods Manufactured
Chart: 
| BOM | Waste | Depreciation | Labor | Other | Total COGS | Gross Margin | Market Price
Running total of $ | 20 | 30 | 50 | 53 | 55
$ Amount | 20 | 10 | 20 | 3 | 2 | 55 | 45 | 100
Material Cost
COGM

## Slide 63: Production Cost Analysis
This section includes materials, labor, and production requirements for the technology.
Bill of Materials
COGS ($)
Material/energy
utilization efficiency
Waste
Stream
1.
Production/Mfc.
Process Flow
2.
Equipment
Machinery
Facilities
CapEx
3.
Utilities
Labor
Rent
OpEx
4.
/amortization

## Slide 64: Bill of Materials (BOM)
Simple Battery Example
Anode
Cathode
Separator
Electrolyte
Housing
Bill of Materials
Cell Materials Costs |  |  | 
Positive Electrode, $/kg |  |  | 
Active material |  |  | 10.00
Carbon |  |  | 6.80
Binder PVDF |  |  | 10.00
Binder Solvent (NMP) |  |  | 3.20
Negative electrode material, $/kg |  |  | 
Active Material |  |  | 19.00
Carbon Black |  |  | 6.80
Binder |  |  | 10.00
Binder Solvent |  |  | 0.00
Positive current collector foil, $/m2 |  |  | 0.80
Negative current collector foil, $/m2 |  |  | 1.80
Separators, $/m2 |  |  | 2.00
Electrolyte, $/L |  |  | 21.60
Actual Numbers
Source: Argonne BatPac v2.0, default values
A list of “ingredients,” or raw materials, chemicals, and components needed to assemble a product.

## Slide 65: Bill of Materials (BOM)
Bill of Materials
A list of “ingredients,” or raw materials, chemicals, and components needed to assemble a product.
Cost Information Sources
Raw material costs (lower bound)
Bulk chemical pricing
Data from reports
Direct supplier research
Vendor discussions for major costs
Actual cost data for projected volumes from specific potential supplies
Direct quote/purchase order
Negotiated contract from vendor
Fidelity
High
Low
Key is to start early and develop iteratively with best available information
CAUTION: Prices for laboratory quantities are much higher than for the commercial quantities that you would use for plant design economic calculations.

## Slide 66: Bill of Materials (BOM)
Bill of Materials
Embodied energy should be taken into account when analyzing materials costs.
Raw
Processed
Fully
Processed
Types of Materials (illustrative example)
Embodied Energy
High
Low
Elements
Proteins
Grains
Chemicals
Parts
Discrete devices
Formed metals

## Slide 67: Process Flow Diagram
  Descriptive step names and step-wise material inputs and outputs
  Establish modeling level of detail: each step to receive its own treatment in production model
  Overall inputs and output define position in value chain
LEGEND
(Stage Number): (Stage Name)
(Material Inputs)
(Stage Output)
PROCESS BLOCK DIAGRAM
1: Make Dough & Form Buns
2: Bake Buns
3: Slice Meat
4: Assemble Sandwiches
5: Toast & Test
Flour
Water
Yeast
Salt
Raw Buns
Herbs
Buns
Meat Block
Sliced Meat
Cheese
Cold
Sandwiches
Toasted Sandwiches
Example: sandwich production line
Process Flow
Capture the entire production process in easily understood format
Source: Sandwich Production Model Template, Stooke

## Slide 68: Process Flow Diagram
  Descriptive step names and step-wise material inputs and outputs
  Establish modeling level of detail: each step to receive its own treatment in production model
  Overall inputs and output define position in value chain
Process Flow
Capture the entire production process in easily understood format
Source: Sandwich Production Model Template, Stooke
Example solar cell manufacturing process

## Slide 69: Capital Expenditure (CapEx)
CapEx
Cost to acquire or upgrade physical assets such as equipment, property, or industrial buildings
What equipment and infrastructure to do I need to run my process?
Capital equipment cost including installation, mil$ |  |  |  | 133
Building, Land and Utilities |  |  |  | 
Area, m2 |  |  |  | 15,928
Cost, $/m2 |  |  |  | 3,000
Building investment, mil$ |  |  |  | 47.8
Capital Equipment, million$ |  |  |  | 40
Simple Battery Example
Source: Argonne BatPac v2.0, default values

## Slide 70: Depreciation = amortized CapEx
The spreading out of capital expenses for assets over a specific time period time (the asset's useful life)
$250M
$25M
$1
Factory &
Equipment
(CapEx)
Yearly
Depreciation
Per-unit
Depreciation
10 yr Term
25M units
Source: 24M Technologies, Inc. 2012

## Slide 71: Operating Expenditures (OpEx)
OpEx
Ongoing cost to run your factory including utilities, labor, rent, etc.

## Slide 72
Performance Analysis
Requisite Operating inputs:
eg. Fuel/Energy
Technology Operating
Performance Characteristics
Efficiency, Lifetime, Capacity Factor
Useful Work/Energy
Output
Relevant Performance Metric
(power, energy, etc.)
Waste
Energy/heat
Can start by making optimistic estimation or performance based on modeling on lab results
Model system physical parameters
Model performance based on changes to those materials
Construct/test prototype
Construct/test pilot demonstration
Test at relevant scale/operating conditions
Make sure you know which performance metrics are valued by the market
  Keep in mind: What is the customer paying for?
Fidelity
High
Low
Building a Performance Model

## Slide 73: Final Step: Integrate Cost & Performance Models
Benefit of technology = value at cost
 | Material A | Material B
COGS ($) | $750 | $1,000
Energy (kWh) | 2 | 2
Life (cycles) | 3,000 | 10,000
Life cycle cost ($/kWh) | $0.13 | $0.05
Cost Model
Integration
Performance Model

## Slide 74: Resources
How do I find chemical/material prices?
How do I determine equipment cost and utilization?
How do I determine labor productivity and wages?

## Slide 75: How do I find chemical/material prices?
ChemE departments at Universities have good resources, here are some to start with:
http://people.clarkson.edu/~wwilcox/Design/refcosts.htm
http://guides.library.tamu.edu/content.php?pid=216817&sid=1802700
http://guides.library.cornell.edu/content.php?pid=2816&sid=14269

## Slide 76: Appendix

## Slide 77: Final Remarks
Get started modeling cost early, and refine as knowledge advances
  guess as placeholder to get framework in place (and make note of it)
  work on larger factors first (getting first significant digit right is a challenge)
Use, manipulate, and adapt the template spreadsheet to suit your needs, but
  be guided by its scope (deliberate)
  don’t dodge necessary considerations because of difficulty to validate or seemingly unfavorable results
Full business financial model (cash flow, debt, timing, etc.) also needed before pitching for external financing (not shown here)
Send any cost modeling questions & comments to your ARPA-E Tech-to-Market Advisor