## Slide 1: A Micro-Systems Enabled Transformation in PV
Michael Haney, Ph.D.
Program Director

## Slide 2: As in Electronics and Photonics, can PV can be transformed by exploiting micro-systems technologies?
Discrete laser/mod/detect circuit
Micro-photonics
Integrated Circuit
Increasing
BW density/J
Increasing Complexity
Discrete Transistor circuit
Micro-electronics Integrated Circuit
Increasing
Ops/J
“Micro-helionics”
Integrated Circuit ??
Increasing
J/$, J/kg
Discrete PV and CPV “circuits”
  It’s all about the Packaging: micro-scale technology provides an effective interface between the macro collection and nano conversion domains.

## Slide 3: Existence proof: Large-area integrated micro-optical/ photonic/electronic systems already exist as commodities
Examples
TFT/LCD displays at 1080p LCD pixels are $500/m2
Touch screen displays for phones, tablets, e-books
FP displays have higher complexity relative to envisioned m-CPV panels
TFT/LCD panels have ~107/m2, 3 color,8-bit active pixels, with 100% yield.
Anticipated m-CPV will have ~105/m2, ~4-6 “color,” DC pixels, with 99% yield.
Can we exploit micro-scale complexity to drive micro-CPV prices to ~$100’s/m2?

## Slide 4: Potential Scaling Benefits for m-CPV 1
Micro-optics mass scaling factor
  Reducing height by factor of N and replacing macro-concentrator with N2 micro-concentrators that have the same collection area reduces overall mass by N.
  Micro-optics performance scaling
    Smaller lenses work better and are easier to fabricate.*
Replace one macro-optical concentrator
With N2 micro-optical concentrators
N
*A. Lohmann, Applied Optics, Vol. 28, No. 23, December, 1989

## Slide 5: Potential Scaling Benefits for m-CPV 2
Thermal management benefits
  Total cell perimeter-to-area ratio scales with N.
Temperature
Nielsen, et al., Fut. PV, May 2010;

## Slide 6
  Access to wider angular spectrum
    Easier (cheaper) to approach Etendue limit (Cmax = n2/sin2a) with micro-optics.
      Cheaper and energy efficient (low mass) collection and tracking options
    Also possible to achieve more concentration of low-angle diffuse light
    Performance improvement of ~0.4-2.3% is possible by increasing acceptance angle from 2o to 5o.*
*G. Agrawal, et al, PVSC 2013
a
Potential Scaling Benefits for m-CPV 3

## Slide 7: Potential Scaling Benefits for m-CPV 4
Interconnect diversity leads to optimized current matching and voltage summing
    Voltage matching provides ~3% improved power conversion efficiency over current matching.*
*A. Lentine, et al, PVSC 2013

## Slide 8: Micro-scale Technical Approach Opportunities
  Better Energy Spectrum Management?
    Integrated spectrum-splitting and concentration concepts.
    Hybrid tandem/lateral concepts.
    Optimized (real-time?) spectrum/electrical power matching.
  Better Angular Spectrum Management?
    Wide-angle low- or medium-concentration concentrator optics.
    Hybrid m-CPV/PV may combine high-efficiency direct and lower-efficiency diffuse energy harvesting.
  Embedded Micro-tracking?
    Various actuation techniques may be considered, depending on architecture.
    Automatic tracking based on micro-scale physics?
Can we exploit these performance scaling benefits AND achieve cost scaling benefits?

## Slide 9
Seattle | Portland | Detroit | Chicago | New York City | Boston | Wilmington | Minneapolis | New Orleans | Atlanta | Miami | Tampa | San Francisco | Los Angeles | Boulder | Honolulu | Fresno | Grand Junction | Reno | Flagstaff | Tonopah | Prescott | Albuquerque | Phoenix | Tucson | Las Vegas | Dagget
Annual Average Global Solar Radiation on a 2-axis tracking system per day (kWh/m2-day)
Chart: Annual Average Solar Radiation (kWh/m2-day)
| 4.9000000000000004 | 5.0999999999999996 | 5.5 | 5.7 | 5.8 | 5.9 | 6 | 6.2 | 6.4 | 6.6 | 6.7 | 6.9 | 7.1 | 7.2 | 7.4 | 7.7 | 7.8 | 8 | 8.2000000000000011 | 8.4 | 8.6 | 8.7000000000000011 | 8.8000000000000007 | 8.9 | 9 | 9.1 | 9.4
Direct Radiation | 2.9 | 3.1 | 3.3 | 3.4 | 3.5 | 3.7 | 3.8 | 4 | 4 | 4.2 | 4 | 4.5 | 5 | 4.8 | 5.4 | 5.2 | 5.6 | 5.9 | 6.2 | 6.4 | 6.7 | 6.8 | 6.7 | 6.8 | 7 | 7.1 | 7.5
Global Radiation | 4.9 | 5.1 | 5.5 | 5.7 | 5.8 | 5.9 | 6 | 6.2 | 6.4 | 6.6 | 6.7 | 6.9 | 7.1 | 7.2 | 7.4 | 7.7 | 7.8 | 8 | 8.2 | 8.4 | 8.6 | 8.7 | 8.8 | 8.9 | 9 | 9.1 | 9.4
Data from: Christian A. Gueymard, Proc. of SPIE Vol. 7046

## Slide 10
Seattle | Portland | Detroit | Chicago | New York City | Boston | Wilmington | Minneapolis | New Orleans | Atlanta | Miami | Tampa | San Francisco | Los Angeles | Boulder | Honolulu | Fresno | Grand Junction | Reno | Flagstaff | Tonopah | Prescott | Albuquerque | Phoenix | Tucson | Las Vegas | Dagget
Annual Average Global Solar Radiation on a 2-axis tracking system per day (kWh/m2-day)
Chart: Annual Average Solar Radiation (kWh/m2-day)
| 4.9000000000000004 | 5.0999999999999996 | 5.5 | 5.7 | 5.8 | 5.9 | 6 | 6.2 | 6.4 | 6.6 | 6.7 | 6.9 | 7.1 | 7.2 | 7.4 | 7.7 | 7.8 | 8 | 8.2000000000000011 | 8.4 | 8.6 | 8.7000000000000011 | 8.8000000000000007 | 8.9 | 9 | 9.1 | 9.4
Direct Radiation | 2.9 | 3.1 | 3.3 | 3.4 | 3.5 | 3.7 | 3.8 | 4 | 4 | 4.2 | 4 | 4.5 | 5 | 4.8 | 5.4 | 5.2 | 5.6 | 5.9 | 6.2 | 6.4 | 6.7 | 6.8 | 6.7 | 6.8 | 7 | 7.1 | 7.5
Diffuse Radiation | 2 | 2 | 2.2 | 2.3 | 2.3 | 2.2 | 2.2 | 2.2 | 2.4 | 2.4 | 2.7 | 2.4 | 2.1 | 2.4 | 2 | 2.5 | 2.2 | 2.1 | 2 | 2 | 1.9 | 1.9 | 2.1 | 2.1 | 2 | 2 | 1.9
Global Radiation | 4.9 | 5.1 | 5.5 | 5.7 | 5.8 | 5.9 | 6 | 6.2 | 6.4 | 6.6 | 6.7 | 6.9 | 7.1 | 7.2 | 7.4 | 7.7 | 7.8 | 8 | 8.2 | 8.4 | 8.6 | 8.7 | 8.8 | 8.9 | 9 | 9.1 | 9.4
Data from: Christian A. Gueymard, Proc. of SPIE Vol. 7046

## Slide 11
Seattle | Portland | Detroit | Chicago | New York City | Boston | Wilmington | Minneapolis | New Orleans | Atlanta | Miami | Tampa | San Francisco | Los Angeles | Boulder | Honolulu | Fresno | Grand Junction | Reno | Flagstaff | Tonopah | Prescott | Albuquerque | Phoenix | Tucson | Las Vegas | Dagget
Annual Average Global Solar Radiation on a 2-axis tracking system per day (kWh/m2-day)
Chart: Annual Average Solar Radiation (kWh/m2-day)
| 4.9000000000000004 | 5.0999999999999996 | 5.5 | 5.7 | 5.8 | 5.9 | 6 | 6.2 | 6.4 | 6.6 | 6.7 | 6.9 | 7.1 | 7.2 | 7.4 | 7.7 | 7.8 | 8 | 8.2000000000000011 | 8.4 | 8.6 | 8.7000000000000011 | 8.8000000000000007 | 8.9 | 9 | 9.1 | 9.4
Direct Radiation | 2.9 | 3.1 | 3.3 | 3.4 | 3.5 | 3.7 | 3.8 | 4 | 4 | 4.2 | 4 | 4.5 | 5 | 4.8 | 5.4 | 5.2 | 5.6 | 5.9 | 6.2 | 6.4 | 6.7 | 6.8 | 6.7 | 6.8 | 7 | 7.1 | 7.5
Diffuse Radiation | 2 | 2 | 2.2 | 2.3 | 2.3 | 2.2 | 2.2 | 2.2 | 2.4 | 2.4 | 2.7 | 2.4 | 2.1 | 2.4 | 2 | 2.5 | 2.2 | 2.1 | 2 | 2 | 1.9 | 1.9 | 2.1 | 2.1 | 2 | 2 | 1.9
Global Radiation | 4.9 | 5.1 | 5.5 | 5.7 | 5.8 | 5.9 | 6 | 6.2 | 6.4 | 6.6 | 6.7 | 6.9 | 7.1 | 7.2 | 7.4 | 7.7 | 7.8 | 8 | 8.2 | 8.4 | 8.6 | 8.7 | 8.8 | 8.9 | 9 | 9.1 | 9.4
% Contribution of Diffuse to Global | 0.40816 | 0.39216 | 0.4 | 0.40351 | 0.39655 | 0.37288 | 0.36667 | 0.35484 | 0.375 | 0.36364 | 0.40299 | 0.34783 | 0.29577 | 0.33333 | 0.27027 | 0.32468 | 0.28205 | 0.2625 | 0.2439 | 0.2381 | 0.22093 | 0.21839 | 0.23864 | 0.23596 | 0.22222 | 0.21978 | 0.20213
Data from: Christian A. Gueymard, Proc. of SPIE Vol. 7046
Projected CPV
domain

## Slide 12
Performance/Cost White-Space Chart for Solar PV
104
1000 750 500 250
Solar Cell System Cost Density ($/m2)
20-year energy production density (kWh/m2)
10 kWh/$
4x103
2x103
6x103
20 kWh/$
2015 1-sun PV (proj.)
CPV, ~40% eff.
(direct radiation)
Utility
Comm.
Tucson
Reno
Current CPV (est.)
8x103
1.2x104
Commercial
Residential
Tucson
Reno
Los Angeles
Minneapolis
Portland
m-CPV potential
Straw man capabilities
35% module eff. (global radiation)
Module cost per m2 same as 1-sun (i.e., 2x less in $/Wp)
50% of BOS cost ~ installed footprint 25% lower $/m2
  Res. Rooftop  ~$1/W
50% increase in constrained-space PV market
Commercial
Utility
Residential
Tucson
Reno
Los Angeles
Minneapolis
Portland
1-Sun PV, 20% module eff.
(global radiation)

## Slide 13
Performance/Mass White-Space Chart for Solar PV
There seems to be a trade-off between performance (energy capture) and system mass
Lower Mass
500
100
100 10 1 .1
Solar Cell Mass Density (Kg/m2)
400
300
200
Av. Power Density Delivered* (W/m2)
**Single junction, 1 sun perf. limit
Smaller Footprint
*Over peak 6 hour period of sunlight
VHESC Phase III goal
CdTe projected
CIGs
Si roof top
1000 sun/ 6 junctions
PowerfilmTM
Polymer projected
** Thermodynamic limit de-rated by 67% to account for practical engineering constraints
** Max. performance limit
** 6 junction/ 25 suns perf. limit
Can we break this paradigm by integrating micro-concentrators and micro-PV cells tiled in dense, flat arrays?
m-CPV
Target Region
400 W/Kg

## Slide 14
What if micro-CPV made it this simple?
Conventional PV
m-CPV
Sample metric | Value
BOS (normalized) | 1
Global Efficiency | 20%
Installed Cost | >1.50 $/W
W/Mass | 200 W/Kg
Sample metric | Value
BOS (normalized) | 3/4
Global Efficiency | 35%
Installed Cost | ~1.00 $/W
W/Mass | 400 W/Kg
Technology disruption does not follow trend lines of current metrics.

## Slide 15: The Heilmeier Questions
What is the problem, why is it difficult? 2. How is it solved today? 3. What is the new technical idea; why can we succeed now? 4. What is the impact if successful? 5. How will the program be organized? 6. How will intermediate results be generated? 7. How will you measure progress? 8. What will it cost and how long will it take?
What are the critical challenges? 2. How is it solved today? 3. What is the new technical idea; why can we succeed now? 4. What will be the impact if successful? (Who cares?) 5. How will the program be organized? 6. How will intermediate results be generated? 7. How will you measure progress? 8. What will it cost and how long will it take?
For this workshop….

## Slide 16: Straw man Goals
~1.75x improvement in flat panel efficiency: 35% of global radiation
~1.75x improvement in panel cost/Watt (maintain cost/area)
Reduce BOS costs by >25%
Expand constrained-space PV market by ??%
  Residential rooftop?
  Commercial?
  Transportation?
  Military?
  Space?
  Other?
What are the most appropriate metrics?
Are these goals legitimate? If not, what should they be?

## Slide 17: Agenda: Thursday, May 8
8:00 AM– 9:00 AM Registration and Breakfast
9:00 AM– 9:15 AM Welcome and Opening Remarks Dr. Eric Rohlfing
9:15 AM– 9:45 AM Workshop Background & Objectives Dr. Mike Haney
9:45 AM– 10:15 AM “Solar Cell Market Evolution
Can we predict the next wave of innovation?” Dr. Jim Rand
10:15 AM– 10:30 AM Coffee Break
10:30 AM–11:00 AM “Exploiting scale effects in photovoltaic cells,
modules, and systems” Dr. Greg Nielson
11:00 AM–11:30 AM “From Novelty to Ubiquity: Challenges & Strategies of
Scaling the LCD Platform” Dr. Pete Bocko
11:30 AM-12:00 PM “An Overview of DoD Military Energy Needs” Ms. Sharon Beermann-Curtin
12:00 PM-12:15 PM Introduction to Breakout 1 Dr. Mike Haney
12:15 PM- 1:15 PM Working Lunch, Breakout 1 (seating by breakout group)
1:15 PM- 2:30 PM Breakout 1, Continued
2:30 PM- 3:00 PM Break
3:00 PM - 4:15 PM Breakout 1, Continued
4:15 PM - 4:30 PM Break
4:30 PM - 5:30 PM Presentation of Breakout 1 Reports by Session Moderators
5:30 PM - 7:30 PM Optional: 15 minute sidebars with Dr. Haney by appt. (sign up with Colleen)

## Slide 18: Agenda: Friday, May 9
7:30 AM- 8:30 AM Breakfast
8:30 AM- 8:45 AM Day 2 Welcome, Breakout 2 Introduction
8:45 AM- 10:00 AM Breakout 2
10:00 AM- 10:30 AM Break
10:30 AM-12:00 PM Breakout 2, Continued
12:00 PM- 1:30 PM Lunch and Presentation of Breakout 2 Reports by Session Moderators
1:30 PM- 2:30 PM Closing Remarks and Open Discussion of Workshop Findings.
2:30 PM- 4:30 PM Optional: 15 minute sidebars with Dr. Haney by appt. (sign up with Colleen)